## Slide 1: Walking and Working Surfaces
Damon Dearmon
National account manager
Safety rail company
Minneapolis, Minnesota
612-500-8504 Cell

## Slide 2: Walking and Working Surfaces
Presentation Objectives
-Define OSHA Safety Standards for Walking and Working Surfaces
-Identify How These Standards Have Recently Changed
-Provide Expertise on How to Remain in Compliance

## Slide 3: Walking and Working Surfaces
OSHA Safety Standards
OSHA Standard 1910
-Addresses slips, trips, and fall hazards in general industry
-Includes surfaces like floors, aisles, stairs, ladders, roofs, platforms, etc.
-Fall protection needed when performing work at least 6 feet but less than 15’ from edge (including guardrails or fall-arrest/fall-restraint systems)
-Ladders – Fall protection guarding is necessary for 4’ or more in elevation change

## Slide 4: Walking and Working Surfaces
OSHA Safety Standards

## Slide 5: Walking and Working Surfaces
Presentation Objectives
2020 TOTALS
Fall Protection – General Requirements (1926.501): 5,424 violations.
Hazard Communication (1910.1200): 3,199.
Respiratory Protection (1910.134): 2,649.
Scaffolding (1926.451): 2,538.
Ladders (1926.1053): 2,129.
Lockout/Tagout (1910.147): 2,065.
11% Reduction from 2019 for falls

## Slide 6: Walking and Working Surfaces
Presentation Objectives
2019 AVERAGE COST
Average cost for medical injury $42,000.00
Average cost per death $1,220,000.00
Average cost to protect a facility $150,000.00 -$175,000.00

## Slide 7: Walking and Working Surfaces
OSHA Safety Standards
Methods for Eliminating Hazards
-Regular Inspections
-Use of fall protection including covers, designated areas, guardrails, handrails, personal fall-protection systems, ladder safety systems, and safety nets

## Slide 8: Walking and Working Surfaces
Updated Standards
OSHA’s Final Rule: Walking and Working Surfaces (Effective Jan. 2017)
-Applies to all general industry entities: purpose is to increase both jobsite safety and consistency between general industry & construction
-Also updated to reflect advances in technology and to incorporate plain language to make final rule easier to understand and follow

## Slide 9: Walking and Working Surfaces
Updated Standards
Specific Regulatory Changes
-Fall Protection Flexibility: Performance-based language allows employers to choose from a range of accepted fall-protection systems
-Added requirements for inspection and maintenance of personal fall- arrest systems

## Slide 10: Walking and Working Surfaces
Updated Standards
Ladder Safety System
-Applies to ladders that extend over 24 feet
-Phase-In: Ladder cages will be phased out over 20-year period, replaced with ladder safety or fall-arrest systems (Deadline: November 18, 2036)
-Final Rule grandfathers in cages and wells on existing ladders, but requires updated standards on new ladders

## Slide 11: Walking and Working Surfaces
Measures to Ensure Compliance
Areas that OSHA considers a hazard
-Elevation changes of more than 4’ (general industry)
-Roof hatches
-Skylights
-Ladders

## Slide 12: Walking and Working Surfaces
Measures to Ensure Compliance

## Slide 13: Walking and Working Surfaces
Measures to Ensure Compliance
OSHA-Compliant Measures to Ensure Safety
-Guardrail Systems
-Warning Line Systems
-Safety Nets
-Personal Fall-Arrest Systems (PFAS)

## Slide 14: Walking and Working Surfaces
Measures to Ensure Compliance
Guardrail System Compliance (1910 Subpart D / 1926 Subpart M)
-Height of 42” (plus or minus 3”) with no opening more than 19”
-Midrail positioned between top edge and walking working surface
-Capable of withstanding 200 pounds of force (150 on midrail)
-Required toeboard when falling objects are present

## Slide 15: Walking and Working Surfaces
Measures to Ensure Compliance
Guardrail System Examples

## Slide 16: Walking and Working Surfaces
Measures to Ensure Compliance
Roof Hatches Skylights Ladders

## Slide 17: Walking and Working Surfaces
Measures to Ensure Compliance
Warning Line System Compliance (1926 Subpart M)
-Flagged at 6-foot (or less) intervals with high-visibility material
-Erected on all sides of work area
-Flag line between 34” and 39” in height
-500-pound tensile strength

## Slide 18: Walking and Working Surfaces
Measures to Ensure Compliance
Warning Line System Examples

## Slide 19: Walking and Working Surfaces
Measures to Ensure Compliance
Professional Assistance with Fall-Protection Projects
-Many companies, including Safety Rail Company, specialize in fall- protection compliance and can offer guidance with your project
-Turn-Key service providers can identify your facility’s fall hazards, engineer a site-specific solution, and install your fall-protection system

## Slide 20: Walking and Working Surfaces
Measures to Ensure Compliance
Things that can be done remotely
-Aerial view CAD Drawing

## Slide 21: Walking and Working Surfaces
Measures to Ensure Compliance
“If you fail to plan, you are planning to fail!”
Benjamin Franklin

## Slide 22: Walking and Working Surfaces
Measures to Ensure Compliance
Thanks very much for your time!